## Slide 1: North Cove Project Update WECAN Meeting August 14, 2024
George Kaminsky, Sumaiya, Hannah Drummond, Amanda Hacking
Notes: REVISED 11/16/2022 - AJ

## Slide 2: Monitoring Methods
Monitoring since 2018 including:
  Topographic surface mapping
  Topographic beach profiles
  Feature mapping
  RFID rock tracking
  Particle sizing
1
2
3
4
5

## Slide 3: Surface Elevation Change in 5-years
5-years Change (2018 - 2023)
Winter 2019
5-years Change (2019 - 2024)
Image: NAIP 2021
Winter 2024
Net Sediment Deposition
295,596 Cubic Yards

## Slide 4: Change in Surface Elevation
5-years Change (2018 - 2023)
Winter 2023
1-year Change (2023 - 2024)
Image: NAIP 2021
Winter 2024
Net Sediment Deposition
70,629 Cubic Yards

## Slide 5
Net Volume Change over 8.25 acres
Time | Net volume change (Cubic Yards) | Average elevation (m) | Average elevation (feet)
2019-2024 | 295,596 | 0.27 | 0.90
2023-2024 | 70,629 | 0.07 | 0.21

## Slide 6: Change in Elevation from last winter
Image: NAIP 2021
̴̴70 feet retreat

## Slide 7: Performance Characteristics
Zone 4
Erosive Revetment
620 m
Zone 5
Dynamically Stable
400 m
Zone 6
Accreting
Spit
400 m
Zone 1
Accreting Dunes + Beach
700 m
Zone 2
Dynamically Stable
200 m
Zone 3
Active
Revetment
300 m
Image: NAIP 2021
2 m NAVD 88 contour

## Slide 8: Zone 1: Dune Development
Profile: 227: Looking west
Profile: 227: Looking landward
Profile: 227: Looking east
Profile 224: View from the top of dynamic revetment
Observations
Stable, 700 m long dune
Mature dune grass (2 - 3 feet high)
Young dune grass (0 - 2 feet high)
Significant growth from 2018 - 2023
Minimum to no maintenance needed
Notes: - Profile 230 to profile 223

## Slide 9: Zone 1: Dune Development
NAVD 88
Image: NAIP 2021

## Slide 10: Zone 2: Dynamically Stable
Profile: 227: Looking west
Profile: 227: Looking landward
Profile: 227: Looking east
Profile 224: View from the top of dynamic revetment
Observations
200 m long dynamically stable area
Eddy current dominates hydrodynamics
Depositional zone for large wood ~20-30 feet long and 3 feet diameter stem
Narrow backshore zone of dune grass in western half
Transition to stable dune
Profile 223 to 222: large wood + dune grass
Profile 222 to 221: large wood only

## Slide 11: Zone 3: Active Revetment

## Slide 12: Zone 4: Erosive Revetment

## Slide 13: Zone 5: Dynamically Stable

## Slide 14: Zone 5: Cobble Berm Development

## Slide 15: Zone 6: Spit Growth
Spit Growth | 
Year | Length from 2023 vegetation line (m)
2018 | 4
2019 | 63.5
2021 | 88.8
2023 | 109.4
3m contour
Image: Ecology 2023

## Slide 16
Conceptual Model
Sediment supply
Sediment bypassing
Managed advance,
dune growth
Managed retreat
Spit growth
Cobble berm growth
Headland feeder bluff

## Slide 17: Conclusions
A modest-scale 2.2 km long quarry spall cobble dynamic revetment and complementary large wood features have halted a rapidly retreating shoreline
Results range from managed advance with developing dunes, high sediment supply, large wood recruitment and dune grass to managed retreat with low sediment supply, low elevation, narrow beach and high cobble transport
Ongoing adaptive management, especially the replenishment of cobble at point sources and increasing upland elevation is essential for maintaining dynamic stability
Ongoing monitoring is essential for informing adaptative management and testing nature-based measures

## Slide 18: Thank you
David Cottrell, Pacific Drainage District #1
Pacific Conservation District
Pacific County
Mott MacDonald
Dave Michalsen, Seattle District U.S. Army Corps of Engineers
Connie Allen, WashAway No More
Shoalwater Bay Tribe
Northwest Association of Networked Ocean Observing Systems (NANOOS)
Paul Bayle, Chris Blenkinsopp, University of Bath
NOAA Office for Coastal Management
Moffatt & Nichol
Washington Department of Ecology Coastal Monitoring & Analysis Program team: Heather Weiner, Diana McCandless, Gabby Alampay, Michelle Gostic, Delaney Stokes, Casey Madill, Kennadie Selden, Alena Reynolds, Alice Henderson
George Kaminsky
gkam461@ecy.wa.gov

## Slide 19: ADA Accessibility
The Department of Ecology is committed to providing people with disabilities access to information and services by meeting or exceeding the requirements of the Americans with Disabilities Act (ADA), Section 504 and 508 of the Rehabilitation Act, and Washington State Policy #188.
To request an ADA accommodation, contact Ecology by phone at 360-407-6831 or email at ecyadacoordinator@ecy.wa.gov. For Washington Relay Service or TTY call 711 or 877-833-6341. Visit Ecology’s website for more information.